## Slide 1: Neuromorphic Computing Midterm Presentation: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
03/11/2021

## Slide 2: Project Timeline

## Slide 3: Corey’s Project Progress
Python Simulations
  High level simulation of model
    Tested model using different hyper parameters
  Frequency analysis of models trained on low pass filter
  Saved weights and biases of trained models
  Optimized model for hardware implementation

## Slide 4: Quick Review
Power Amplifier
RFTuner
ADC
Antenna
Digital Mixer
Digital Local Oscillator
Lowpass Filter
Signal Processing
Implemented on FPGA

## Slide 5: Quick Review
Power Amplifier
RFTuner
ADC
Antenna
Digital Mixer
Digital Local Oscillator
Lowpass Filter
Signal Processing
Observer
Neural Network
Implemented on FPGA
Training

## Slide 6: Quick Review
Power Amplifier
RFTuner
ADC
Antenna
Digital Mixer
Digital Local Oscillator
Lowpass Filter
Signal Processing
Observer
Neural Network
Trojan
Error
Trained Network

## Slide 7: Quick Review
Power Amplifier
RFTuner
ADC
Antenna
Digital Mixer
Digital Local Oscillator
Lowpass Filter
Signal Processing
Observer
Neural Network
Implemented on FPGA

## Slide 8: Quick Review
Power Amplifier
RFTuner
ADC
Antenna
Digital Mixer
Digital Local Oscillator
Signal Processing
Observer
Neural Network
Implemented on FPGA

## Slide 9: SDR Digital Front End
Digital Down Converter (DDC)

## Slide 10: What A DDC Does
ADCs typically sample at a very high frequency
  Requires an unnecessarily fast DSP since the data we are concerned about is usually much lower frequency
DDC lowers the frequency the digitized signal
  Still preserves the original signal
  Reduces DSP speed requirements
Down conversion is used to demodulate AM signals

## Slide 11: On Off Keying (OOK)
A type of Amplitude Modulation
Presence of the carrier wave denotes a ’1’
Absence of the carrier wave denotes a ‘0’

## Slide 12: Down Conversion Example Using OOK Data
Mixer
Lowpass Filter

## Slide 13: Generating Data
Generate a binary signal modulated using OOK
  Create a random bitstream array (e.g. [0 1 0 0 1 0 1 1 0 1 0 1 0 0 1 1])
  Create an empty NumPy array
  Loop through bitstream appending a linear signal for ‘0’ and a sine wave for ‘1’ to the array

## Slide 14: Generating Data
Model a DDC using SciPy and NumPy
  Mixer multiplies modulated signal with carrier sine wave
  Low pass FIR filter removes high frequency component

## Slide 15: Lowpass FIR Filter
Carrier
Frequency
(500kHz)
Cutoff
Frequency
(100kHz)

## Slide 16
Observer
Neural Network

## Slide 17: Model Architecture Block Diagram
1-D CNN Layer
(64 Filters)
x[n]
x[n-64]
x[n-1]
…
Input
Dense Layer
(50 Units)
Output
(1 Unit)
y[n]
Max Pooling
(window size = 2)
Flatten

## Slide 18: Training Procedure
Generate OOK data
  x_train = mixer output
  y_train = lowpass output
Train for ~500 epochs with Adadelta optimizer
  Finds local minimums fast
Train for ~250 epochs with Adam optimizer (learning rate = 1e-5)
  Reduces loss even further without overfitting
Graphical visualization of optimizer performance. Adapted from “LSTM Optimizer Choice?” by Bikal Basnet, 2016, retrieved from https://deepdatascience.wordpress.com/2016/11/18/which-lstm-optimizer-to-use/[5]

## Slide 19: Results OOK Low Pass Filter Dataset

## Slide 20: Results Audio Low Pass Filter Dataset

## Slide 21: Results OOK Mixer Dataset

## Slide 22: Conclusion
The Model works but its effectiveness is dependent on the dataset
  Has difficulty changing a constant signal to a sine wave
Does the model understand the component functionality?

## Slide 23: Frequency Response Comparison
Determine how well the CNN models the low pass filter’s functionality
Input a set of sine waves (1kHz – 1MHz) to each model variation
Get the magnitude using the following equation:

## Slide 24
Chart: Frequency Response of Different Model Variations
| 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000 | 80000 | 90000 | 100000 | 200000 | 300000 | 400000 | 500000 | 600000 | 700000 | 800000 | 900000
Low Pass Filter | -0.00096744 | -0.0021733 | -0.0038698 | -0.0060466 | -0.0086936 | -0.011831 | -0.015425 | -0.019558 | -0.024189 | -0.096794 | -0.21759 | -0.38641 | -0.60664 | -0.87346 | -1.1907 | -1.5583 | -1.9768 | -2.4511 | -10.2093 | -25.2086 | -56.1948 | -87.2829 | -87.2666 | -88.4203 | -88.5278 | -88.8266
CNN32128 | -1.0558 | -1.0562 | -1.0567 | -1.0573 | -1.0581 | -1.059 | -1.0602 | -1.0615 | -1.0629 | -1.088 | -1.1327 | -1.1954 | -1.2766 | -1.3767 | -1.4993 | -1.6597 | -1.8338 | -2.0219 | -4.9761 | -10.3244 | -14.2544 | -34.208 | -13.9139 | -9.7093 | -10.7925 | -17.258
CNN64128 | -1.4753 | -1.4766 | -1.4785 | -1.481 | -1.4841 | -1.4879 | -1.4923 | -1.497 | -1.5013 | -1.5629 | -1.6779 | -1.8567 | -2.0839 | -2.3685 | -2.7503 | -3.2122 | -3.7393 | -4.3397 | -13.4592 | -19.6852 | -24.2401 | -39.0554 | -24.7997 | -24.4718 | -23.4777 | -15.706
CNNAudio | -0.95394 | -0.95422 | -0.95512 | -0.95666 | -0.95917 | -0.96265 | -0.96713 | -0.97224 | -0.97754 | -1.0544 | -1.1886 | -1.3801 | -1.6408 | -1.9522 | -2.3358 | -2.8053 | -3.3374 | -3.9334 | -12.9818 | -28.7655 | -27.4355 | -33.7288 | -35.9828 | -24.4628 | -28.1208 | -23.0763

## Slide 25: Potential Issues With Current Configuration
Project goal: implement matrix multiplication operations in convolutional layer using FeFETs
2 Issues
  64 filters in CNN layer
    Weights & biases = 99,493
    More filters means more area taken by FeFET circuit
  Data type = float (32b)
    Input size (bitwise) exponentially increases area taken by FeFET circuit

## Slide 26: Float to Half
half = 16b = float/2
  float: 0.12345678
  half: 0.1235
Reducing the precision of the input, weights and biases = much smaller circuit area
Accuracy of the network is not sacrificed
Evaluation speed slightly increased (191ms  147ms)

## Slide 27: Results: Float to Half

## Slide 28: Reducing Filters
Less filters = less operations
  More speed (which is great in an SDR application)
  Reduces size of matrix multiplication circuit
  Using 8 filters  weights & biases = 5,737 << 99,493
  Evaluation speed further increased (147ms  88ms)

## Slide 29: Results: Reducing Filters OOK Dataset

## Slide 30: Results: Reducing Filters OOK Dataset

## Slide 31: Future Project Deliverables
Implement CNN in:
  FPGA
  Jetson Nano
Confirm FeFET output accuracy
Benchmark performance of FPGA and Jetson Nano Convolutional layer against FeFET implementation