## Slide 1: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
04/27/2021

## Slide 2: Project Timeline

## Slide 3: Project Summary
Machine learning model
  Learn SDR component functionality by training on input/output signal data
  Implemented using a one-dimensional convolutional neural network (1DCNN)
Goal: compare 3 implementations of the convolutional layer
  SoC (Jetson Nano)
  FPGA
  MMA (Neuromorphic Hardware)

## Slide 4: FPGA CNN Acceleration Summary
FPGA allows you to program hardware circuits for specified functionality
  Allows for the implementation of parallelism
CNNs utilize the convolution operation (multiplication and addition)
These operations can be implemented as circuits allowing for each operation to be done in parallel

## Slide 5: FPGA Conv2 Block Diagram
Conv2
16
Input0
16
Input1
16
Filter0
16
Filter1
32
Output
Output = (Input0 * Filter0) + (Input1 * Filter1)

## Slide 6: FPGA Implementation
Conv2
Conv2
Conv2
…
Output0
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Output1
Output31
4 Filters
Each Conv2 block implements a hardware circuit used to multiply and add the 4 16-bit numbers
Each number in the feature maps can now be computed in parallel as opposed to serially

## Slide 7: Final Project Contributions
Concluded FPGA development
  Implemented bias in Conv layer filters
  Expanded model from 8 input samples to 32 input samples
    Explored pros and cons of using floating vs fixed point precision
  Benchmarked FPGA Conv layer using sample input data from Python script

## Slide 8: Implementing Bias
CNN filters also have an additional parameter, called a bias, that is added to the resulting convolution
CNN

## Slide 9: FPGA Implementation With Bias
Conv2
16
Input0
16
Input1
16
Filter0
16
Filter1
16
Bias
32
Output
Output = (Input0 * Filter0) + (Input1 * Filter1) + Bias

## Slide 10: Scaling the Model
To easily test functionality, the model was scaled down
  Input size: 32 samples  8 samples
  Sample data type: 16-bit float  8-bit integer
Problem: scaling up requires the implementation of floating point arithmetic

## Slide 11: Floating Point Binary Representation
Floats are represented in binary in 3 sections:
  Sign: Indicates the sign (-/+)
  Exponent: Used to compute the exponent portion of the number
  Fraction: Used to compute the fractional portion of the number

## Slide 12: Floating Point Binary Example
sign = 1
exponent = 27 + 21 + 20 = 128 + 2 + 1 = 131
fraction = 2-1 = 0.5
Number = (-1)1 x (1 + 0.5) x 2131– 127 = -24.0

## Slide 13: Floating Point Arithmetic
Can’t be done in the way integer arithmetic can
Requires more complex hardware
  Higher utilization
  Increased circuit delay
  Not enough time to implement :(

## Slide 14: Solution: Use VHDL ”real” type
Instead of using logic vectors to represent floats use “real” type
  VHDL’s float type
  Can just do normal arithmetic without complex hardware implementation (e.g. y <= a*b)

## Slide 15: Results

## Slide 16: Conclusion
Accurate to the python simulations
  Average mean squared error = 0
VHDL real types cannot be synthesized!
  Only for simulation purposes
  Even though this design is simple to implement and accurate it cannot be used on a real FPGA

## Slide 17: Fixed Point Arithmetic
Decimal number is represented by 2 integers
  Integer part
  Fractional part
Allows for the use of integer arithmetic
  Simpler hardware
  Faster
  Less space required to store values
Comes at the loss of precision
  Might not be entirely needed given our application

## Slide 18: FPGA Fixed Point Implementation
Each input is now a 16-bit signed fixed point value
  1-bit sign
  2-bit integer part
    Doesn’t need to be as big considering most values range from -1 to 1
  13-bit fractional part
Output is still 32 bits but is divided similarly to the input
  1-bit sign
  4-bit integer part
  27-bit fractional part

## Slide 19: Results: Utilization and Timing

## Slide 20: Results: Accuracy
Python FeatureMap[0] = -0.13936129
Binary value outputted = 0 0000 00010001001101010001111011(2)  0.03361(10)
Inaccuracy could potentially be due to the following:
  Issues in converting from float to fixed point
  Misuse of the ”signed” VHDL data type
  Overflow

## Slide 21: Final Thoughts
Areas of functional improvement
  Implement floating point arithmetic
  Fix issues with fixed point arithmetic and compare to float implementation
FPGA acceleration of CNN shows promising results