## Slide 1: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
04/01/2021

## Slide 2: Project Timeline

## Slide 3: SDR Implementation Block Diagram
Power Amplifier
RFTuner
ADC
Antenna
Digital Mixer
Digital Local Oscillator
Lowpass Filter
Signal Processing
Observer
Neural Network
Error
Trained Network
Analog
Digital
RF Front End
Digital Front End
FPGA
MMA/SoC/FPGA
Serial

## Slide 4: Model Architecture
x(t)
x(t-64)
x(t-1)
…
CNN Layer
Input
Dense Layer
(50 Units)
Output
(1 Unit)
y(t)
Max Pooling
Flatten

## Slide 5: Model Architecture
x(t)
x(t-64)
x(t-1)
…
CNN Layer
Input
Dense Layer
(50 Units)
Output
(1 Unit)
y(t)
Max Pooling
Flatten

## Slide 6: Conv Layer Hardware Implementations
3 Implementations:
  MMA (HSpice)
  SoC (Jetson Nano)
  FPGA (Zynq-7000)
Feed inputs through each implementation and compare throughput
CNN

## Slide 7: Implementing Conv Layer
Model was previously simulated in Python
Implementing the conv layer requires the weights of the Python model and the ability to verify output to a given input

## Slide 8: Python Script
Outputs the weights of a given model
Creates a set of input and output data to verify implementations

## Slide 9: Jetson Nano
Nvidia’s low power ARM computer built specifically for inferencing
Runs on Linux (easy to port TensorFlow model)
Supports PCIe

## Slide 10: Implementation Progress
Imported the model using TensorFlow
Generated input data
Tested model functionality (it works!)
Obtained throughput: 816.59 samples/s
  Not great compared to MacBook (44903.46 samples/s)
  Vanilla TensorFlow is not optimized for Jetson Nano hardware

## Slide 11: TensorRT
Nvidia’s API for accelerating inferencing models on Jetson Nano
  Boasts 6x performance boost
  Documentation is not great
    Currently working on freezing the model

## Slide 12: Future Project Deliverables
Implement TensorRT and see if it improves throughput
Implement model on FPGA

## Slide 13: Josh’s Project Progress
MMA circuit design
  Fully implemented 2bitx3bit multiplication.
  Decoding circuitry for word-line loading
  Sense-amplifiers and counters at the end of the bit lines
  Adders, multipliers, decoders, flip-flops to perform the necessary arithmetic to get the final answer
MMA circuit HSPICE simulations

## Slide 14: Block Diagram of simulated MMA
Encoding inputs as voltage sources
Decoder for word-line loading
Sense amps on bit-lines
Counters (BSC)
Adders to adjust counting value
Multiply by bit-position
Capture values in DFFs
Shift and add DFFs
Final answer in binary

## Slide 15: Josh’s Project Progress
Input encoding
  No changes here since last update
  Each bit of input is a separate voltage source
  I would like to change this to be parallelly loaded into registers
Word line decoding
  Word lines are loaded based on a clock-cycle counter (BRC) and after the sense-amps have been pre-charged
Sense-amps
  No changes here since last update
BSC for sense-amp
  A binary synchronous counter has been added to the output of the sense-amps in order to keep track of the AND operations
Adding to adjust counting value
  I need to shift the MSBs of each counter output to the next counter and add them together
Multiplication of count value by the appropriate bit-place
  This is done by using the clock counting and a decoder
The multiplied values are captured in flip-flops, then shifted and added together

## Slide 16: Circuit Simulation
 | a1 | b1 | a2 | b2
Decimal | 3 | 7 | 3 | 7
Binary | 11 | 111 | 11 | 111
 | clk: 3-4 | clk: 1-2
a1 | 1 | 1
a2 | 1 | 1
1
1
1
1
b12
b21
b11
b21
SA1
SA2
WL0
WL1
BL2
BL1
1
1
b10
b20
SA0
BL0
(3*7)+(3*7) = 42
clk1 | 1 | 1 | 1
clk2 | 10 | 10 | 10
clk3 | 1 | 1 | 1
clk4 | 10 | 10 | 10

## Slide 17: Circuit Simulation
clk1 | 1 | 1 | 1
clk2 | 10 | 10 | 10
clk3 | 1 | 1 | 1
clk4 | 10 | 10 | 10
10 10 10
1
+10
11
1
+10
11
clk: 1-2 | 1 | 1 | 1 | 0 | = 14*20
clk: 3-4 | 1 | 1 | 1 | 0 | = 14*21
11 1 0
(14*20)+(14*21) = 42

## Slide 18: Circuit Simulation
WL1
WL0
SE
CAP
F5
 | a1 | b1 | a2 | b2
Decimal | 3 | 7 | 3 | 7
Binary | 11 | 111 | 11 | 111
 | clk: 3-4 | clk: 1-2
a1 | 1 | 1
a2 | 1 | 1
1
1
1
1
b12
b21
b11
b21
SA1
SA2
WL0
WL1
BL2
clk1
BL1
clk2
clk3
clk4
1
1
b10
b20
SA0
BL0
CLK
F4
F3
F2
F1
F0
clk | F5 | F4 | F3 | F2 | F1 | F0
1 | 0 | 1 | 1 | 1 | 1 | 1
2 | 0 | 1 | 1 | 1 | 1 | 1
3 | 1 | 0 | 1 | 1 | 1 | 0
4 | 1 | 0 | 1 | 1 | 1 | 0
5 | 1 | 0 | 1 | 0 | 1 | 0

## Slide 19: Performance Metrics

## Slide 20: Future Project Deliverables
MMA architecture utilizing FeFETs
  Extend weights to full 16-bit width (Bit/Source lines), and full 96 weights (Word line)
  Drop trained weights into FeFET crossbar
  Mapping of the input values to vectors for MMA
    Load in inputs into registers then utilize existing one-hot vector decoder to load each value on the word-lines
  Finalize circuit-level SPICE simulations
  Interface with python simulations