## Slide 1: Neuromorphic Computing Midterm Presentation: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
(513) 225-7917
04/27/2021

## Slide 2: Project Timeline

## Slide 3: Project Summary
Machine learning model
  Learn SDR component functionality by training on input/output signal data
  Implemented using a one-dimensional convolutional neural network (1DCNN)
Goal: compare 3 implementations of the convolutional layer
  SoC (Jetson Nano)
  FPGA
  MMA (Neuromorphic Hardware)

## Slide 4: FPGA CNN Acceleration Summary
FPGA allows you to program hardware circuits for specified functionality
  Allows for the implementation of parallelism
CNNs utilize the convolution operation (multiplication and addition)
These operations can be implemented as circuits allowing for each operation to be done in parallel

## Slide 5: FPGA Conv2 Block Diagram
Conv2
16
Input0
16
Input1
16
Filter0
16
Filter1
32
Output
Output = (Input0 * Filter0) + (Input1 * Filter1)

## Slide 6: FPGA Implementation
Conv2
Conv2
Conv2
…
Output0
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Output1
Output31
4 Filters
Each Conv2 block implements a hardware circuit used to multiply and add the 4 16-bit numbers
Each number in the feature maps can now be computed in parallel as opposed to serially

## Slide 7: Final Project Contributions
Concluded FPGA development
  Implemented bias in Conv layer filters
  Expanded model from 8 input samples to 32 input samples
    Explored pros and cons of using floating vs fixed point precision
  Benchmarked FPGA Conv layer using sample input data from Python script

## Slide 8: Implementing Bias
CNN filters also have an additional parameter, called a bias, that is added to the resulting convolution
CNN

## Slide 9: FPGA Implementation With Bias
Conv2
16
Input0
16
Input1
16
Filter0
16
Filter1
16
Bias
32
Output
Output = (Input0 * Filter0) + (Input1 * Filter1) + Bias

## Slide 10: Scaling the Model
To easily test functionality, the model was scaled down
  Input size: 32 samples  8 samples
  Sample data type: 16-bit float  8-bit integer
Problem: scaling up requires the implementation of floating point arithmetic

## Slide 11: Floating Point Binary Representation
Floats are represented in binary in 3 sections:
  Sign: Indicates the sign (-/+)
  Exponent: Used to compute the exponent portion of the number
  Fraction: Used to compute the fractional portion of the number

## Slide 12: Floating Point Binary Example
sign = 1
exponent = 27 + 21 + 20 = 128 + 2 + 1 = 131
fraction = 2-1 = 0.5
Number = (-1)1 x (1 + 0.5) x 2131– 127 = -24.0

## Slide 13: Floating Point Arithmetic
Can’t be done in the way integer arithmetic can
Requires more complex hardware
  Higher utilization
  Increased circuit delay
  Not enough time to implement :(

## Slide 14: Solution: Use VHDL ”real” type
Instead of using logic vectors to represent floats use “real” type
  VHDL’s float type
  Can just do normal arithmetic without complex hardware implementation (e.g. y <= a*b)

## Slide 15: Results

## Slide 16: Conclusion
Accurate to the python simulations
  Average mean squared error = 0
VHDL real types cannot be synthesized!
  Only for simulation purposes
  Even though this design is simple to implement and accurate it cannot be used on a real FPGA

## Slide 17: Fixed Point Arithmetic
Decimal number is represented by 2 integers
  Integer part
  Fractional part
Allows for the use of integer arithmetic
  Simpler hardware
  Faster
  Less space required to store values
Comes at the loss of precision
  Might not be entirely needed given our application

## Slide 18: FPGA Fixed Point Implementation
Each input is now a 16-bit signed fixed point value
  1-bit sign
  2-bit integer part
    Doesn’t need to be as big considering most values range from -1 to 1
  13-bit fractional part
Output is still 32 bits but is divided similarly to the input
  1-bit sign
  4-bit integer part
  27-bit fractional part

## Slide 19: Results: Utilization and Timing

## Slide 20: Results: Accuracy
Python FeatureMap[0] = -0.13936129
Binary value outputted = 0 0000 00010001001101010001111011(2)  0.03361(10)
Inaccuracy could potentially be due to the following:
  Issues in converting from float to fixed point
  Misuse of the ”signed” VHDL data type
  Overflow

## Slide 21: Final Thoughts
Areas of functional improvement
  Implement floating point arithmetic
  Fix issues with fixed point arithmetic and compare to float implementation
FPGA acceleration of CNN shows promising results

## Slide 22: FeFET-MMA Summary
The FeFET-MMA is meant to perform the convolution operation in hardware for the purpose of accelerating the calculation
MMA architecture is based on the idea of performing digital AND operations on the input and weight bits using the weight encoded as variable threshold voltage FeFETs
The outputs of the AND operations are tracked and counted, and fed into combinational and sequential logic to determine the final convoluted answer
FeFET VT | Input (Gate) | Output
High (0) | 0 | Low Current (0)
High (0) | 1 | Low Current (0)
Low (1) | 0 | Low Current (0)
Low (1) | 1 | High Current (1)
VG
ID
High VT
Low VT

## Slide 23: Block Diagram of MMA
Encoding inputs as voltage sources
Decoder for word-line loading
Sense amps on bit-lines
Counters (BSC)
Adders to adjust counting value
Multiply by bit-position
Capture values in DFFs
Shift and add DFFs
Add filter bias
Spice netlist is ~1500 lines of code
Implements four kernel filters
  Each has two 16bit weights, operates on two 16bit inputs
Final answer in binary

## Slide 24: MMA Architecture
Kernel 0
Kernel 1
Kernel 2
Kernel 3
36bit output
16bit input
16bit input
36bit output
36bit output
36bit output

## Slide 25: MMA Architecture
Crossbar
Peripheral Control Circuitry
Final Bias Adder
16bit input
16bit input
36bit output
16bit bias
2bits
16bits
35bits

## Slide 26: MMA Architecture
Controller
16bit
16bit
35bits
SA Array
SA Counters
SA Adder
Bit-place Multiplier
Bit-place Decoder
DFF-1 Array
DFF-2 Array
DFF Adder
Word-line Decoder
Crossbar
16bits
2bits
Clk
Counters

## Slide 27: Caveats
I made a number of assumptions throughout this project about how the binary numbers that are fed into the circuit are formatted that dictated how the circuit was designed
  Unsigned binary numbers
  Integer operations
As a result, it cannot handle negative numbers without overhauling the design
It also cannot properly handle fractional numbers
  With more time I could implement this thoroughly
  In the meantime I do have a temporary workaround in place

## Slide 28: Caveats – Floating Point Operation Workaround
Example:
  W0 = 0.23426208
  W1 = 0.6055579
  Bias = 0.00364347
  I0 = 0.254150390625
  I1 = 0
  Convolution =
We can multiply each component by some constant value to allow for integer operations, at the cost of some precision.
We have 16 bits available for binary representation, so the maximum number is 65536
  Multiple each term by 106 and distribute it out evenly to weights and inputs
  Convolution =
  The answer can be divided by 106 to get 0.063079

## Slide 29: Simulation Setup
Modified | Filter 0 | Filter 1 | Filter 2 | Filter 3
Weight0 | 234 | 550 | 245 | 381
Weight1 | 606 | 35 | 774 | 455
Bias | 3643 | 16176 | 14210 | 6968
Original | Filter 0 | Filter 1 | Filter 2 | Filter 3
Weight0 | 0.23426208 | 0.549507 | -0.24479 | -0.38059
Weight1 | 0.6055579 | -0.03461 | 0.773546 | -0.45489
Bias | 0.00364347 | 0.016176 | 0.01421 | 0.006968
Original | Test 0 | Test 1 | Test 2 | Test 3 | Test 4
Input0 | 0.254150390625 | 0.33447265625 | 0.40771484375 | 0.454833984375 | 0.47021484375
Input1 | 0 | 0.254150390625 | 0.33447265625 | 0.40771484375 | 0.454833984375
Modified | Test 0 | Test 1 | Test 2 | Test 3 | Test 4
Input0 | 254 | 334 | 408 | 455 | 470
Input1 | 0 | 254 | 334 | 408 | 455

## Slide 30: Simulation Results - Accuracy
Of the 20 convolution operations, 11 were correct
Of the 9 that are incorrect, the average error is 0.299%
  Each answer is off by 512
  1 bit place: 29 is stuck at 0
Expected | Test 0 | Test 1 | Test 2 | Test 3 | Test 4
Filter0 | 63079 | 235723 | 301519 | 357361 | 389353
Filter1 | 155876 | 208766 | 252266 | 280706 | 290601
Filter2 | 76440 | 292636 | 372686 | 441477 | 481530
Filter3 | 103742 | 249792 | 314386 | 365963 | 393063
Actual | Test 0 | Test 1 | Test 2 | Test 3 | Test 4
Filter0 | 62567 | 235723 | 301519 | 356849 | 389353
Filter1 | 155876 | 208524 | 252266 | 280706 | 290089
Filter2 | 75928 | 292124 | 372174 | 441477 | 481530
Filter3 | 103742 | 249280 | 314386 | 365963 | 392551

## Slide 31: Simulation Results - Speed
Simulated speed
  It takes 4 clock cycles per bit of input to process the convolution operation
    2 for word-line loading
    1 for capturing values from flip-flops
    1 for resetting counter flip-flops
  At 16 bits, this results in 64 clock cycles/convolution operation
  Clock is 200MHz
  , 9.6µs for 4 full feature maps
Simulation time
  For 4 parallel convolution operations on 2 16bit numbers, the HSPICE simulation takes 30 minutes, and >1GB of memory.
  This means for 4 full feature maps, it would take 15 hours of simulation time.

## Slide 32: Simulation Results - Comparisons
SoC: ~12,500 samples/second
FPGA: ~66,000,000 samples/second
  Simulated 100% accuracy, but implementation suffered
FeFET: ~416,667 samples/second
  Simulated ~99% accuracy, but implementation suffered

## Slide 33: Final Thoughts
Areas of functional improvement
  Floating point operation
    This will involve changing how the binary numbers are fed into the matrix, as well as the multiplier for bit place determination
    Attention must be paid to the mantissa and exponent components of the binary number, with appropriate shifting to align with other inputs and weights
    Each set of clock cycles that is loading the IX bits to the matrix is calculating the 2X bit of the final answer
    To represent fractional numbers, the values will need to be right-shifted to account for negative exponents
  Negative numbers
Areas of optimization
  Bit-place overhead
  Capacitive loading
    Assumption is generic load capacitors; this could be tuned based on fan-out
  Transistor sizing
  Speed
  Low power design
    There’s some erroneous signal switching that could be reduced
    Clock gating to reduce unnecessary state changes