## Slide 1: Neuromorphic Computing Midterm Presentation: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
(513) 225-7917
04/27/2021

## Slide 2: FeFET-MMA Summary
The FeFET-MMA is meant to perform the convolution operation in hardware for the purpose of accelerating the calculation
MMA architecture is based on the idea of performing digital AND operations on the input and weight bits using the weight encoded as variable threshold voltage FeFETs
The outputs of the AND operations are tracked and counted, and fed into combinational and sequential logic to determine the final convoluted answer
FeFET VT | Input (Gate) | Output
High (0) | 0 | Low Current (0)
High (0) | 1 | Low Current (0)
Low (1) | 0 | Low Current (0)
Low (1) | 1 | High Current (1)
VG
ID
High VT
Low VT

## Slide 3: Block Diagram of MMA
Encoding inputs as voltage sources
Decoder for word-line loading
Sense amps on bit-lines
Counters (BSC)
Adders to adjust counting value
Multiply by bit-position
Capture values in DFFs
Shift and add DFFs
Add filter bias
Spice netlist is ~1500 lines of code
Implements four kernel filters
  Each has two 16bit weights, operates on two 16bit inputs
Final answer in binary

## Slide 4: MMA Architecture
Kernel 0
Kernel 1
Kernel 2
Kernel 3
36bit output
16bit input
16bit input
36bit output
36bit output
36bit output

## Slide 5: MMA Architecture
Crossbar
Peripheral Control Circuitry
Final Bias Adder
16bit input
16bit input
36bit output
16bit bias
2bits
16bits
35bits

## Slide 6: MMA Architecture
Controller
16bit
16bit
35bits
SA Array
SA Counters
SA Adder
Bit-place Multiplier
Bit-place Decoder
DFF-1 Array
DFF-2 Array
DFF Adder
Word-line Decoder
Crossbar
16bits
2bits
Clk
Counters

## Slide 7: Caveats
I made a number of assumptions throughout this project about how the binary numbers that are fed into the circuit are formatted that dictated how the circuit was designed
  Unsigned binary numbers
  Integer operations
As a result, it cannot handle negative numbers without overhauling the design
It also cannot properly handle fractional numbers
  With more time I could implement this thoroughly
  In the meantime I do have a temporary workaround in place

## Slide 8: Caveats – Floating Point Operation Workaround
Example:
  W0 = 0.23426208
  W1 = 0.6055579
  Bias = 0.00364347
  I0 = 0.254150390625
  I1 = 0
  Convolution =
We can multiply each component by some constant value to allow for integer operations, at the cost of some precision.
We have 16 bits available for binary representation, so the maximum number is 65536
  Multiple each term by 106 and distribute it out evenly to weights and inputs
  Convolution =
  The answer can be divided by 106 to get 0.063079

## Slide 9: Simulation Setup
Modified | Filter 0 | Filter 1 | Filter 2 | Filter 3
Weight0 | 234 | 550 | 245 | 381
Weight1 | 606 | 35 | 774 | 455
Bias | 3643 | 16176 | 14210 | 6968
Original | Filter 0 | Filter 1 | Filter 2 | Filter 3
Weight0 | 0.23426208 | 0.549507 | -0.24479 | -0.38059
Weight1 | 0.6055579 | -0.03461 | 0.773546 | -0.45489
Bias | 0.00364347 | 0.016176 | 0.01421 | 0.006968
Original | Test 0 | Test 1 | Test 2 | Test 3 | Test 4
Input0 | 0.254150390625 | 0.33447265625 | 0.40771484375 | 0.454833984375 | 0.47021484375
Input1 | 0 | 0.254150390625 | 0.33447265625 | 0.40771484375 | 0.454833984375
Modified | Test 0 | Test 1 | Test 2 | Test 3 | Test 4
Input0 | 254 | 334 | 408 | 455 | 470
Input1 | 0 | 254 | 334 | 408 | 455

## Slide 10: Simulation Results - Accuracy
Of the 20 convolution operations, 11 were correct
Of the 9 that are incorrect, the average error is 0.299%
  Each answer is off by 512
  1 bit place: 29 is stuck at 0
Expected | Test 0 | Test 1 | Test 2 | Test 3 | Test 4
Filter0 | 63079 | 235723 | 301519 | 357361 | 389353
Filter1 | 155876 | 208766 | 252266 | 280706 | 290601
Filter2 | 76440 | 292636 | 372686 | 441477 | 481530
Filter3 | 103742 | 249792 | 314386 | 365963 | 393063
Actual | Test 0 | Test 1 | Test 2 | Test 3 | Test 4
Filter0 | 62567 | 235723 | 301519 | 356849 | 389353
Filter1 | 155876 | 208524 | 252266 | 280706 | 290089
Filter2 | 75928 | 292124 | 372174 | 441477 | 481530
Filter3 | 103742 | 249280 | 314386 | 365963 | 392551

## Slide 11: Simulation Results - Speed
Simulated speed
  It takes 4 clock cycles per bit of input to process the convolution operation
    2 for word-line loading
    1 for capturing values from flip-flops
    1 for resetting counter flip-flops
  At 16 bits, this results in 64 clock cycles/convolution operation
  Clock is 200MHz
Simulation time
  For 4 parallel convolution operations on 2 16bit numbers, the HSPICE simulation takes 30 minutes, and >1GB of memory.
  This means for 4 full feature maps, it would take 15 hours of simulation time.

## Slide 12: Final Thoughts
Areas of functional improvement
  Floating point operation
    This will involve changing how the binary numbers are fed into the matrix, as well as the multiplier for bit place determination
    Attention must be paid to the mantissa and exponent components of the binary number, with appropriate shifting to align with other inputs and weights
    Each set of clock cycles that is loading the IX bits to the matrix is calculating the 2X bit of the final answer
    To represent fractional numbers, the values will need to be right-shifted to account for negative exponents
  Negative numbers
Areas of optimization
  Bit-place overhead
  Capacitive loading
    Assumption is generic load capacitors; this could be tuned based on fan-out
  Transistor sizing
  Speed
  Low power design
    There’s some erroneous signal switching that could be reduced
    Clock gating to reduce unnecessary state changes