## Slide 1: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
04/15/2021

## Slide 2: Project Timeline

## Slide 3: FPGA Conv Layer Acceleration
Convolution is just a series of multiplications and summations
On traditional processors those operations are performed serially
FPGA can be used to accelerate the execution of math operations
CNN

## Slide 4: FPGA Implementation
Conv2
16
Input0
16
Input1
16
Filter0
16
Filter1
32
Output
Output = (Input0 * Filter0) + (Input1 * Filter1)

## Slide 5: FPGA Implementation
Conv2
Conv2
Conv2
…
Output0
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Conv2
Output1
Output31
4 Filters
Each conv block implements a hardware circuit used to multiply and add the 4 16-bit numbers
Each number in the feature maps can now be computed in parallel as opposed to serially

## Slide 6: FPGA Simulation
Started with 8 integer input samples
  Model is effective with >= 32 input samples
  Uses halfs instead of ints
Input = [0, 1, 2, 3, 4, 5, 6, 7, 8]
Filters: F0 = [1, 1], F1 = [2, 2], F2 = [3, 3], F3 = [4, 4]
Outputs:
  O0 = [0*1 + 1*1, 1*1 + 2*1,…, 7*1 + 8*1] = [ 1 , 3 ,…, 15 ]
  O1 = [0*2 + 1*2, 1*2 + 2*2,…, 7*2 + 8*2]
  O2 = [0*3 + 1*3, 1*3 + 2*3,…, 7*3 + 8*3]
  O3 = [0*4 + 1*4, 1*4 + 2*4,…, 7*4 + 8*4]

## Slide 7: FPGA Simulation Results

## Slide 8: Utilization and Timing

## Slide 9: Conclusion
MUCH much faster than Jetson Nano implementation (~15ns << ~23µs)
Comes at the sacrifice of package size
  Needs a lot more IO
    Higher end FPGAs support much more IO (Virtex-6 goes up to 1200)
  Network parameters can be reduced to help shrink size (less filters, smaller input size etc.)

## Slide 10: Future Project Deliverables
Scale FPGA implementation to allow for 32 input samples
Develop a python script that can convert the filter and input values to std_logic_vectors for test bench
Benchmark FPGA implementation