## Slide 1: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
04/01/2021

## Slide 2: Project Timeline

## Slide 3: SDR Implementation Block Diagram
Power Amplifier
RFTuner
ADC
Antenna
Digital Mixer
Digital Local Oscillator
Lowpass Filter
Signal Processing
Observer
Neural Network
Error
Trained Network
Analog
Digital
RF Front End
Digital Front End
FPGA
SoC/FPGA
Serial

## Slide 4: Model Architecture
x(t)
x(t-64)
x(t-1)
…
CNN Layer
Input
Dense Layer
(50 Units)
Output
(1 Unit)
y(t)
Max Pooling
Flatten

## Slide 5: Model Architecture
x(t)
x(t-64)
x(t-1)
…
CNN Layer
Input
Dense Layer
(50 Units)
Output
(1 Unit)
y(t)
Max Pooling
Flatten

## Slide 6: Conv Layer Hardware Implementations
3 Implementations:
  MMA (HSpice)
  SoC (Jetson Nano)
  FPGA (Zynq-7000)
Feed inputs through each implementation and compare throughput
CNN

## Slide 7: Implementing Conv Layer
Model was previously simulated in Python
Implementing the conv layer requires the weights of the Python model and the ability to verify output to a given input

## Slide 8: Python Script
Outputs the weights of a given model
Creates a set of input and output data to verify implementations

## Slide 9: Jetson Nano
Nvidia’s low power ARM computer built specifically for inferencing
Runs on Linux (easy to port TensorFlow model)
Supports PCIe

## Slide 10: Implementation Progress
Imported the model using TensorFlow
Generated input data
Tested model functionality (it works!)
Obtained throughput: 816.59 samples/s
  Not great compared to MacBook (44903.46 samples/s)
  Vanilla TensorFlow is not optimized for Jetson Nano hardware

## Slide 11: TensorRT
Nvidia’s API for accelerating inferencing models on Jetson Nano
  Boasts 6x performance boost
  Documentation is not great
    Currently working on freezing the model
    Requires TF 1.15.3 (<2.3.1)

## Slide 12: Future Project Deliverables
Implement TensorRT and see if it improves throughput
Implement model on FPGA