## Slide 1: Neuromorphic Computing Midterm Presentation: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
02/18/2021

## Slide 2: Project Timeline

## Slide 3: Corey’s Project Progress
Python Simulations
  Simulated DDC SDR circuit and tested against model
  Frequency analysis of models trained on low pass filter
  Tested model using different hyper parameters

## Slide 4: SDR Digital Front End
Digital Down Converter (DDC)

## Slide 5: What A DDC Does
ADCs typically sample at a very high frequency
  Requires an unnecessarily fast DSP since the data we are concerned about is usually much lower frequency
DDC lowers the frequency the digitized signal
  Still preserves the original signal
  Reduces DSP speed requirements
Down conversion is used to demodulate AM signals

## Slide 6: On Off Keying (OOK)
A type of Amplitude Modulation
Presence of the carrier wave denotes a ’1’
Absence of the carrier wave denotes a ‘0’

## Slide 7: Down Conversion Example Using OOK Data
Mixer
Lowpass Filter

## Slide 8: Generating Data
Generate a binary signal modulated using OOK
  Carrier frequency = 500kHz
Model a DDC using SciPy (Python)
  Mixer multiplies modulated signal with oscillator signal
  Low pass FIR filter removes high frequency component

## Slide 9: Lowpass FIR Filter
Carrier
Frequency
(500kHz)
Cutoff
Frequency
(100kHz)

## Slide 10
Observer
Neural Network

## Slide 11: Model Architecture Block Diagram
1-D CNN Layer
(64 Filters)
x[n]
x[n-64]
x[n-1]
…
Input
Dense Layer
(50 Units)
Output
(1 Unit)
y[n]
Max Pooling
(window size = 2)
Flatten

## Slide 12: Training Procedure
Generate OOK data
  x_train = mixer output
  y_train = lowpass output
Train for ~500 epochs with Adadelta optimizer
  Finds local minimums fast
Train for ~250 epochs with Adam optimizer (learning rate = 1e-5)
  Reduces loss even further without overfitting
Graphical visualization of optimizer performance. Adapted from “LSTM Optimizer Choice?” by Bikal Basnet, 2016, retrieved from https://deepdatascience.wordpress.com/2016/11/18/which-lstm-optimizer-to-use/[5]

## Slide 13: Results OOK Low Pass Filter Data

## Slide 14: Results Audio Low Pass Filter Data

## Slide 15: Results OOK Mixer Data

## Slide 16: Conclusion
The Model works but its effectiveness is dependent on the dataset
  Has difficulty changing a constant signal to a sine wave
Does the model understand the component functionality?

## Slide 17: Frequency Response Comparison
Determine how well the CNN models the low pass filter’s functionality
Input a set of sine waves (1kHz – 1MHz) to each model variation
Get the magnitude using the following equation:

## Slide 18
Chart: Frequency Response of Different Model Variations
| 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000 | 80000 | 90000 | 100000 | 200000 | 300000 | 400000 | 500000 | 600000 | 700000 | 800000 | 900000
Low Pass Filter | -0.00096744 | -0.0021733 | -0.0038698 | -0.0060466 | -0.0086936 | -0.011831 | -0.015425 | -0.019558 | -0.024189 | -0.096794 | -0.21759 | -0.38641 | -0.60664 | -0.87346 | -1.1907 | -1.5583 | -1.9768 | -2.4511 | -10.2093 | -25.2086 | -56.1948 | -87.2829 | -87.2666 | -88.4203 | -88.5278 | -88.8266
CNN32128 | -1.0558 | -1.0562 | -1.0567 | -1.0573 | -1.0581 | -1.059 | -1.0602 | -1.0615 | -1.0629 | -1.088 | -1.1327 | -1.1954 | -1.2766 | -1.3767 | -1.4993 | -1.6597 | -1.8338 | -2.0219 | -4.9761 | -10.3244 | -14.2544 | -34.208 | -13.9139 | -9.7093 | -10.7925 | -17.258
CNN64128 | -1.4753 | -1.4766 | -1.4785 | -1.481 | -1.4841 | -1.4879 | -1.4923 | -1.497 | -1.5013 | -1.5629 | -1.6779 | -1.8567 | -2.0839 | -2.3685 | -2.7503 | -3.2122 | -3.7393 | -4.3397 | -13.4592 | -19.6852 | -24.2401 | -39.0554 | -24.7997 | -24.4718 | -23.4777 | -15.706
CNNAudio | -0.95394 | -0.95422 | -0.95512 | -0.95666 | -0.95917 | -0.96265 | -0.96713 | -0.97224 | -0.97754 | -1.0544 | -1.1886 | -1.3801 | -1.6408 | -1.9522 | -2.3358 | -2.8053 | -3.3374 | -3.9334 | -12.9818 | -28.7655 | -27.4355 | -33.7288 | -35.9828 | -24.4628 | -28.1208 | -23.0763

## Slide 19: Problems With Current Configuration
64 filters in CNN layer
  Weights & biases = 99,493
  More filters means more area taken by FeFET circuit
Data type = float (32b)
  Input size (bitwise) exponentially increases area taken by FeFET circuit

## Slide 20: Float to Half
Half = 16b = float/2
Reducing the data type of the input, weights and biases would significantly reduce the circuit area
Accuracy of the network is not sacrificed

## Slide 21: Results: Float to Half

## Slide 22: Reducing Filters
Less filters = less operations
  More speed (which is great in an SDR application)
  Reduces size of matrix multiplication circuit
  Using 8 filters  weights & biases = 5,737 << 99,493

## Slide 23: Results: Reducing Filters

## Slide 24: Future Deliverables
Implement CNN in:
  FPGA
  Jetson Nano
Confirm FeFET output accuracy
Benchmark performance of FPGA and Jetson Nano Convolutional layer against FeFET implementation