## Slide 1: Neuromorphic Computing Midterm Presentation: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
(513) 225-7917
04/15/2021

## Slide 2: Project Timeline

## Slide 3: Josh’s Project Progress
MMA circuit design and HSPICE simulations
  Extended weights to full 16-bit length
  Architectural level changes and optimizations
    Made the crossbar and peripheral circuitry their own subcircuits, to enable simultaneous kernel operation simulations
      Trade off is area vs. speed
    Began making changes to the controller for the capture and reset signals due to errors introduced by the weight bit extension

## Slide 4: Block Diagram of simulated MMA
Encoding inputs as voltage sources
Decoder for word-line loading
Sense amps on bit-lines
Counters (BSC)
Adders to adjust counting value
Multiply by bit-position
Capture values in DFFs
Shift and add DFFs
Final answer in binary
This is where the capture and reset signals are being generated and utilized
  Capture values from multiplier
  Reset counters for the sense-amplifiers

## Slide 5: Timing Comparison
Capture with delayed reset in one clock cycle.
  3 clock cycles/bit of input = 3*16 = 48 clock cycles/sample.
  Clock frequency had to be slowed down from initial simulations to 100 Mhz.
Capture and reset signals are each set in their own respective clock cycles.
  5 clock cycles/bit of input = 5*16 = 80 clock cycles/sample.
  I haven’t tested the upper limit of the clock frequency yet, but from past simulations, I know 200 Mhz can work.

## Slide 6: HSPICE Simulation
WL0
WL1
SE
CLK
Capture
Reset

## Slide 7: HSPICE Simulation
CLK
Capture
Reset
Multiplier Outputs

## Slide 8: HSPICE Simulation
CLK
Capture
Reset
Final Outputs

## Slide 9: Performance Metrics
Problems in area/power consumption calculations
  Translation of HSPICE to Verilog/VHDL for Synopses Design Vision/Power Compiler
    HSPICE is an analog circuit simulator using transistor level netlists
    Verilog/VHDL are purely digital circuit simulators using gate level designs
    The standard cell library I have access to does not have variable threshold voltage level transistors available
    My design doesn’t use standard cells, as I needed to alter the widths of various transistors in certain gates

## Slide 10: Future Project Deliverables
MMA architecture utilizing FeFETs
  Finish changing the capture and reset signal controller to individual clock cycles
  Drop trained weights into FeFET crossbar
  Finalize circuit-level SPICE simulations
Final Report and Presentation
  Compare results between FPGA, Jetson Nano, and FeFET MMA implementations