## Slide 1: Neuromorphic Computing Midterm Presentation: FPGA Hardware Acceleration of CNN based SDR Analysis
Corey L. Butts, Joshua Mayersky
buttscl@mail.uc.edu, mayersjd@mail.uc.edu
(330) 883-9679
(513) 225-7917
04/01/2021

## Slide 2: Project Timeline

## Slide 3: Josh’s Project Progress
MMA circuit design
  Fully implemented 2bitx3bit multiplication.
  Decoding circuitry for word-line loading
  Sense-amplifiers and counters at the end of the bit lines
  Adders, multipliers, decoders, flip-flops to perform the necessary arithmetic to get the final answer
MMA circuit HSPICE simulations

## Slide 4: Block Diagram of simulated MMA
Encoding inputs as voltage sources
Decoder for word-line loading
Sense amps on bit-lines
Counters (BSC)
Adders to adjust counting value
Multiply by bit-position
Capture values in DFFs
Shift and add DFFs
Final answer in binary

## Slide 5: Josh’s Project Progress
Input encoding
  Each bit of input is a separate voltage source
  I would like to change this to be parallelly loaded into registers
Word line decoding
  Word lines are loaded based on a clock-cycle counter (BRC) and after the sense-amps have been pre-charged
Sense-amps
  No changes here since last update
BSC for sense-amp
  A binary synchronous counter has been added to the output of the sense-amps in order to keep track of the AND operations
Adding to adjust counting value
  I need to shift the MSBs of each counter output to the next counter and add them together
Multiplication of count value by the appropriate bit-place
  This is done by using the clock counting and a decoder
The multiplied values are captured in flip-flops, then shifted and added together

## Slide 6: Circuit Simulation
 | a1 | b1 | a2 | b2
Decimal | 3 | 7 | 3 | 7
Binary | 11 | 111 | 11 | 111
 | clk: 3-4 | clk: 1-2
a1 | 1 | 1
a2 | 1 | 1
1
1
1
1
b12
b21
b11
b21
SA1
SA2
WL0
WL1
BL2
BL1
1
1
b10
b20
SA0
BL0
(3*7)+(3*7) = 42
clk1 | 1 | 1 | 1
clk2 | 10 | 10 | 10
clk3 | 1 | 1 | 1
clk4 | 10 | 10 | 10

## Slide 7: Circuit Simulation
clk1 | 1 | 1 | 1
clk2 | 10 | 10 | 10
clk3 | 1 | 1 | 1
clk4 | 10 | 10 | 10
10 10 10
1
+10
11
1
+10
11
clk: 1-2 | 1 | 1 | 1 | 0 | = 14*20
clk: 3-4 | 1 | 1 | 1 | 0 | = 14*21
11 1 0
(14*20)+(14*21) = 42

## Slide 8: Circuit Simulation
WL1
WL0
SE
CAP
F5
 | a1 | b1 | a2 | b2
Decimal | 3 | 7 | 3 | 7
Binary | 11 | 111 | 11 | 111
 | clk: 3-4 | clk: 1-2
a1 | 1 | 1
a2 | 1 | 1
1
1
1
1
b12
b21
b11
b21
SA1
SA2
WL0
WL1
BL2
clk1
BL1
clk2
clk3
clk4
1
1
b10
b20
SA0
BL0
CLK
F4
F3
F2
F1
F0
clk | F5 | F4 | F3 | F2 | F1 | F0
1 | 0 | 1 | 1 | 1 | 1 | 1
2 | 0 | 1 | 1 | 1 | 1 | 1
3 | 1 | 0 | 1 | 1 | 1 | 0
4 | 1 | 0 | 1 | 1 | 1 | 0
5 | 1 | 0 | 1 | 0 | 1 | 0

## Slide 9: Performance Metrics

## Slide 10: Future Project Deliverables
MMA architecture utilizing FeFETs
  Extend weights to full 16 bit width (Bit/Source lines), and full 96 weights (Word line)
  Drop trained weights into FeFET crossbar
  Mapping of the input values to vectors for MMA
    Load in inputs into registers then utilize existing one-hot vector decoder to load each value on the word-lines
  Finalize circuit-level SPICE simulations
  Interface with python simulations

## Slide 11: References
[1] Ding, R., Tian, X., Bai, G., Su, G. & Wu, X. Hardware implementation of convolutional neural network for face feature extraction. in Proceedings of International Conference on ASIC (IEEE Computer Society, 2019). doi:10.1109/ASICON47005.2019.8983575
[2] Dong, Z. et al. Convolutional Neural Networks Based on RRAM Devices for Image Recognition and Online Learning Tasks. IEEE Transactions on Electron Devices 66, 793–801 (2019).
[3] Soloviev, R., Telpukhov, D., Mkrtchan, I., Kustov, A. & Stempkovskiy, A. Hardware Implementation of Convolutional Neural Networks Based on Residue Number System. in Moscow Workshop on Electronic and Networking Technologies, MWENT 2020 - Proceedings (Institute of Electrical and Electronics Engineers Inc., 2020). doi:10.1109/MWENT47943.2020.9067498
[4] Park, B., Ishiwara, H., Okuyama, M., Sakai, S., Yoon, S. Ferroelectric-Gate Field Effect Transistor Memories Device Physics and Applications. in Topics in Applied Physics 131, (2020).
[5] Valueva, M. V., Nagornov, N. N., Lyakhov, P. A., Valuev, G. V. & Chervyakov, N. I. Application of the residue number system to reduce hardware costs of the convolutional neural network implementation. Mathematics and Computers in Simulation 177, 232–243 (2020).
[6] Chung, J., Choi, W., Park, J. & Ghosh, S. Domain Wall Memory-Based Design of Deep Neural Network Convolutional Layers. IEEE Access 8, 19783–19798 (2020).
[7] Yao, P. et al. Fully hardware-implemented memristor convolutional neural network. Nature 577, 641–646 (2020).
[8] Gong, L., Wang, C., Li, X., Chen, H. & Zhou, X. MALOC: A fully pipelined FPGA accelerator for convolutional neural networks with all layers mapped on chip. IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems 37, 2601–2612 (2018).
[9] Solovyev, R. A., Stempkovsky, A. L. & Telpukhov, D. V. Study of Fault Tolerance Methods for Hardware Implementations of Convolutional Neural Networks. Optical Memory and Neural Networks (Information Optics) 28, 82–88 (2019).
[10] Hacene, G. B., Gripon, V., Arzel, M., Farrugia, N. & Bengio, Y. Quantized guided pruning for efficient hardware implementations of deep neural networks. in NEWCAS 2020 - 18th IEEE International New Circuits and Systems Conference, Proceedings 206–209 (Institute of Electrical and Electronics Engineers Inc., 2020). doi:10.1109/NEWCAS49341.2020.9159769
[11] Gysel, P. Ristretto: Hardware-Oriented Approximation of Convolutional Neural Networks. (2016).
[12] Chen, W., Wang, Y., Yang, C. & Li, Y. Hardware acceleration implementation of three-dimensional convolutional neural network on vector digital signal processors. in 2020 4th International Conference on Robotics and Automation Sciences, ICRAS 2020 122–129 (Institute of Electrical and Electronics Engineers Inc., 2020). doi:10.1109/ICRAS49812.2020.9135062
[13] Long, Y., Na, T., Rastogi, P., Rao, K., Khan, A., Yalamanchili, S., Mukhopadhyay, S. A ferroelectric FET based power-efficient architecture for data-intensive computing. IEEE/ACM International Conference on Computer-Aided Design, Digest of Technical Papers, ICCAD, (2018). doi:10.1145/3240765.3240770
[14] Long, Y., Kim, D., Lee, E., Saha, P., Mudassar, Burhan A., She, X., Khan, A., Mukhopadhyay, S. A Ferroelectric FET-Based Processing-in-Memory Architecture for DNN Acceleration. IEEE Journal on Exploratory Solid-State Computational Devices and Circuits, 5, 2, 113-122 (2019). doi: 10.1109/JXCDC.2019.2923745
[15] Long, Y., Lee, E., Kim, D., Mukhopadhyay, S. Flex-PIM: A Ferroelectric FET based Vector Matrix Multiplication Engine with Dynamical Bitwidth and Floating Point Precision. Proceedings of the International Joint Conference on Neural Networks (2020). doi: 10.1109/IJCNN48605.2020.9206672.
[16] Shalini, Kumar, A., Design Of High Speed And Low Power Sense Amplifier for SRAM Applications. International Journal of Scientific & Engineering Research. 4, 7, 402-406 (2013).
[17] Okobiah, O., Mohanty, S.P., Kougianos, E., Poolakkaparambil, M. Towards Robust Nano-CMOS Sense Amplifier Design: A Dual-Threshold versus Dual-Oxide Perspective in ACM Great Lakes Symposium on VLSI, GLSVLSI, Proceedings 145-150 (2011).